2 db Physiological-Biological Temperature Controller TMP-5b

Technical data:

The controlled temperature range: 0 Centigrade to 120 Centigrade, in 1 Centigrade steps

The resolution of the measurement: 0.1 Centigrade

Histheresis (approximately): 0.3 - 0.5 Centigrade. The actual histheresis depens on the thermal capacity, and the heat drain used on the heated object.

Both internal (built into the heated object), and external temperature sensors can be used. The internal/external sensor selector switch is located at the back side of the Physiological - Biological Temperature Controller.

Display: 4 x 16 characters alphanumeric LCD with bright blue backlight

Programming: three pushbuttons on the front, in menu system

Automatic internal diagnostic algorithm in the software

Flash program memory

Non-volatile EEPROM memory to store the parameters used last time

Temperature sensor (either in internal or external arrangement): DS18S20 from Dallas Semiconductor

2 db Heating pad with stainless steel top plate for small animals (compatible with the 12 V Physiological – Biological Tempeature Controller, with built-in digital DS1820 temperature sensor) 170x115 mm