Technical Specification:

120 pieces of cassette holder rack for Liconic Biobank system

Micronic M96-2 0,75 cassette holder

Main parts:

1) Frame bent into a U profile:

- Shape: U profile with angled reinforcement at the bottom.

- In the middle of the 2 sides of the U profile, there are reinforcement bends outwards for reinforcement and spacing.

- U profile end of the cassette body is bent back outwards, which ensures parallel alignment when inserting the cassette.

- The cassettes are held in place by tabs folded out of the U-profile plate.

- There are 6 pieces of these tabs per cassette, the inner tab has a locking function and it holds the loaded M96-2 cassette.

- The bent frame is 1300 mm long and can hold 22 M96-2 cassettes

- External dimensions: 139 mm x 100 mm x 1300 mm

- Internal dimensions: 130 mm x 89 mm

- Cassette size: 127.8 mm x 85.5 mm x 37.8 mm

- Material: KO36 Ti, thickness of 1 mm, stainless steel plate

2) Closing part (sealing element): 2 pieces

- It is mounted with screw fixing at the end of the U profile

- It is bent at an angle so that when it is inserted in the cold storage it guides the cassette holder into place and also ensures parallelism of the U profile

- Material: KO36 Ti, thickness of 2 mm, steel plate

- Size: 89 mm x 130 mm x 20 mm

3) Thermo sheet: 1 piece

- Provides thermal insulation of the vertically inserted metal holder

- Fixed to the closing part by a screw joint, the insertion is locked to the housing by a slightly tapered shoulder joint

- Material: XPS-100

- Size: according to the sample product

4) Magnetic sheet: 1 piece

- Magnetic sheet with screw fastening on top of the cassette holder

- Size: 100 mm x 100 mm x 3 mm

- Material: ferritic steel

>>>>Please consult the contact person before constructing your official quotation — thank you.<<<<

>>>>The winner bidder must undertake to consult the customer on the exact parameters of the products before production.<<<<

Terms of delivery:

Please deliver the manufactured products in groups of 24 pieces, delivery scheduled based on prior consultation with the customer.

Delivery deadline: 30/06/2024

We accept partial invoicing based on the delivered products.