Technical specification of 3 pairs of fiber coupled lasers, listed in Call for Proposal # SZTE/2020/PB10551

Version of  04/02/2020

Product name: 6 pcs. lasers:

- center wavelengths at 25 °C: 448.06 +- 0.2 nm

Optical output power: min. 80mW (25°C)

Spectral Width (FWHM): 2.0 nm

Operating temperature: 10-70 °C

Recommend operating temperature: 25 °C

Operating voltage: max 6.5V

Operating current: max 165mA

Packaging: TO56 package

Threshold Current: max. 60 mA

Operating Voltage: max. 7 V

Beam Divergence (FWHM): max. 11 x 25 deg

Polarization 100:1

Thermal resistance (junction to case): 34 – K/W

Offers to be submitted on the website of the Call for the Proposal .

Please include shipping cost in your offer.

Please note that offers must fully match the criteria listed above. Offers for products with less specification and quantities will be considered invalid.

Date: 04/02/2020

Please upload your offer on the website of the Call for the Proposal, 
No SZTE/2020/PB10551