Technical specification of Call for proposals No SZTE/2021/PB11892 
for Hydrogen tank

Mass of hydrogen stored at 60 bar (15°C): minimum 4.2 kg

Temperature of use: from -40 °C to 65 °C

Maximum working pressure (PS): 60 bar

Maximum refilling pressure: 60 bar

Position of use: vertical in a rack

Inner volume: minimum 850 L

External dimensions (without support): Ø 84 cm x 187 cm

Tank support frame: simple

Orifice diameter: 60 mm

Hydrogen tank materials: polymer liner reinforced with composite material

Specifications of the valve: 2 threads ¼” BSPP female → Ø orifice = 6 mm

TPRD activation temperature: 110 °C

Service life: minimum 20 years / 10,000 cycles

Certified according to European directive PED.

Equipped with on the bottom of one plug and on the upper side a valve and PRV 60 bar max.

Mounted on simple standard frame with strips and protections.

Formal requirements of the quotations.  Please include these data in your proposal:

- Please refer to SZTE/2021/PB11892

- Name of the bidder company, address. Please note that the bidder's company name must be same as that of the invoicing company (In case the bidder company outsources the invoicing, please notify us before the tender deadline)

- The price for the product + all the expenses (e.g. shipping to Szeged, Hungary; handling etc.) of the purchase. Please note that in case shipping/handling cost is not clearly listed in the offer, we will assume that the total cost includes shipping/handling cost, and no further shipping/handling cost can be charged.

- Please list unit prices, subtotals and total

- Please do not list the bank charge (to be paid by customer).

- Terms of delivery and delivery/lead time.

- Terms of payment (such as: net 30 or net 60 or prepayment). Our University prefers to pay with wire transfer.

- Quote validity and/or quote issue date. The quotation should be preferably valid for 60 days, due to excessive evaluation period, but at least for 30 days.

  - Quote validity day should be not earlier than the deadline of the procedure.

  - Quote issue date should not be earlier than the starting date of the call for proposals.

- Please include the specification in your offer (so that it can be clearly evaluated whether it matches all the specified features).

- Warranty and guarantee terms if applicable.

Date: 25 of October, 2021.

Please upload your offer on the website of the Call for the Proposals, No SZTE/2021/PB11892