Specifikáció

Ohaus MULTI PRO FC5816R (OHAU30314818) – 1 db

- Speed Range: 200 rpm – 16,000 rpm

- Maximum Relative Centrifuge Force (x g): 24325 g

- Maximum Capacity(Rotor): 6 x 250 ml

- Refrigeration Range: -4 °F – 104 °F (-20 °C – 40 °C)

- Program memories: 99

- Rotor In Package: Not applicable

- Acceleration Gear: 10

- Deceleration Gear: 10

- Dimensions: 21.18 in x 13.94 in x 28.46 in (538 mm x 354 mm x 723 mm) (LxHxW)

- Display: LCD with backlight

- Lid lock: Motor driven

- Net Weight: 170 lb (77 kg)

- Noise Level: ≤63±2 dB(A)

- Power: AC Power (Included)

- Power Consumption: 785 W

- Pre-cool time: From room temperature to 4℃ ＜ 10min

- Rotor Compatibility: Angle 4 x 85ml RB ID Hi;  Angle 6 x 250 ml FB ID;  Angle 44 x 1.5 / 2.0 ml ID V2;  Angle 30 x 15 ml RB/FA ID;  Angle 6 x 50 ml RB ID Hi;  Rotor Angle 24x1.5/2.0ml ID BIOSEALS V1;  Angle 10 x 50 ml FA ID;  Angle 20 x 10 ml RB ID Hi;  Angle 6 x 85 ml RB ID;  Swing out 16 x 50 ml ID;  Swing out 4 x 250 ml ID;  Swing out 2 x 3MTP ID

- Rotor Recognition Method: Auto

- Running Time: Continous;  Quickspin;  10 sec to 99 h 59 min 59 sec

- Safety Certification: CE;  FCC

- Working Environment: 36°F – 95°F, 80%RH, non-condensing (2°C – 35°C, 80%RH, non-condensing)

Lengőrotor FC5816R centrifugához (OHAU30314828) – 1 db

Tartókosár 4 x 50 ml Falcon csőhöz (OHAU30304375) – 2 db

Tartókosár 10 x 15 ml Falcon csőhöz (OHAU30314583) – 2 db

Tartókosár 12 x 4-10 ml, 16 mm-es csőhöz (OHAU30314585) – 2 db

Tartókosár 14 x 5-7 ml, 13 mm-es átmérőjű vérvételi csőhöz (OHAU30314584) – 2 db

Szögrotor 24 x 1.5/2.0ml csövekhez (R-A24X2/16MIB; CatNo.: 83041238) – 1 db

Az ajánlati árnak tartalmaznia kell a szállítás és a beüzemelés költségeit!