Part „A” - Gold rods

Technical specifications:

Gold rods are to be quoted that meets or exceeds the following technical specifications:

Material:

Gold (Au)

Purity should be 99.9% or better. (Please state it in your quote.)

Shape and dimensions:

Shape: rod

Diameter: 3 mm (or 1/8")

Length: 20 mm (or nearest bigger if this size can not be met)

Quantity: 4 pcs

Requirements: The metals should be supplied with a certificate stating the purity and/or contaminants.

Part „B” – Optical filter

Technical specifications:

| Description | Quantity |
| --- | --- |
| 390 nm blocking edge BrightLine® short-pass filter Transmission band: 320 – 370 nm (Tavg > 70%) Edge wavelength: 378 nm Blocking band: 390 – 1100 nm (ODavg > 5) Diameter: 25 mm Thickness: 3.5 mm | 1 |

Part „C” – Vacuum components

Technical specifications:

| Description | Material | Quantity |
| --- | --- | --- |
| Clamp for elastomer seal, flange size ISO-KF DN40 | Al alloy | 10 |
| Centering ring and O-ring, flange size ISO-KF DN40 | SS/Fluorocarbon | 10 |
| Blank flange, flange size ISO-KF DN40 | SS | 10 |
| Oil mist eliminator, compact open-body design, inlet/outlet: KF25, flow: 20 scmf | Mixed | 2 |
| Replacement element for oil mist eliminator (compact open-body design, inlet/outlet: KF25, flow: 20 scmf) | Mixed | 2 |

Part „D” – Optical and optomechanical components I.

| Description | Quantity |
| --- | --- |
| Solid aluminum breadboard, 600 mm x 600 mm x 12.7 mm, M6 threads on 25 mm centers (metric) | 1 |
| Solid aluminum breadboard, 600 mm x 900 mm x 12.7 mm, M6 threads on 25 mm centers (metric) | 1 |
| SMA to SMA mating sleeve for connecting SMA-terminated optical fibers | 10 |
| Metal cap for SMA mating sleeves (Caps protect bulkheads and mating sleeves) | 10 |
| FC/PC to SMA fiber optic mating sleeve (mate an FC/PC-terminated fiber to an SMA-terminated fiber) | 2 |
| SMA bulkhead adapter with lock nut | 5 |
| Precision fiber cleaning fluid (Sticklers™ Fiber Optic Splice & Connector Cleaner or similar) | 1 |
| XY Translating Lens Mount for Ø1" optics up to 0.39" thick, ±1 mm travel in X and Y via 3/16"-100 or finer Adjusters, SM1 threading, Compatible with Thorlabs’s 30 mm Cage System | 1 |
| SM1-Threaded Kinematic Mount for thin Ø1" optics up to 0.14" (3.6 mm) thick, Angular Range: ±4°, Resolution: 8 mrad (0.5°) per rev via Two 1/4"-80 Precision Adjusters | 1 |
| Cosine Corrector for SMA-connectorized fiber, External SM05 threads, 0.5 mm diffuser thickness, 4 mm clear aperture | 1 |
| Bifurcated fiber bundle, Ø105 µm core, 0.22 NA, Low OH content, SMA connectors, each arm is 2 m in length | 1 |
| SM1-Threaded Mount, Ø25 mm UV fused silica reflective metallic ND Filter, OD: 1.0 | 1 |
| f=50.0 mm, Ø1" UV fused silica bi-convex lens, Uncoated | 1 |

Part „E” – Optical and optomechanical components II.

The following solarisation resistant optical fibers are to be quoted:

| Description | Quantity |
| --- | --- |
| 1-out-of-7 bifurcated fiber (reflection probe) with Ø105 µm, silica high-OH (250-1200 nm) fibers, each arm is 2 m in length excitation arm: SMA 905 termination, 1x105 µm detection arm: SMA 905 termination, 6x105 µm. common end: SMA 905 termination, closely-hexagonally packed 7x105 µm configuration; | 1 |
| Ø400 µm core silica, high OH optical fiber with SMA 905 termination at both ends, 30 m length | 1 |
| Ø400 µm core silica, high OH optical fiber with SMA 905 termination at both ends, 15 m length | 1 |
| Ø400 µm core silica, high OH optical fiber with SMA 905 termination at both ends, 5 m length | 4 |
| Ø400 µm core silica, high OH optical fiber with SMA 905 termination at both ends, 0.5 m length | 4 |