The LT3000 microplate strip washer

Fully automated washing improves intra and inter plate reproducibility and minimises the number of failed experiments.

Flexible programming with up to 50 userdefined protocols allows wash parameters to be optimised for all assays.

Washes all standard flat, round and vbottom 96 well plates.

Monitoring of waste liquid level with automatic shut-off to prevent spillage of potentially biohazardous waste.

Both 8 and 12 way wash manifolds included.

Double aspiration facility to minimise residual volume in flat bottomed plates.

Dispense Precision		    CV < 2%

Residual Volume 		           < 2 ml

Wash Volume 		    50 – 3,000 ml (8 way manifold)

50 – 2,000 ml (12 way manifold)

Wash Cycles 			    Up to 10

Soak Time 			    0 – 10 hours

Plate Types 			    96 well flat, round and vbottom

Bottle Capacity		    2 l

Memory 			    50 user-defined wash protocols

Display 			    5” LCD

Power Supply 			    AC 220V ± 10%, 50 – 60 Hz

Net Weight 			    8 Kg

Dimensions L x W x H (mm)   390 x 340 x 180 (excluding bottles)