Leica DM IL LED Fluo Stand Mikroszkóp alkatrészek

Minden tételből 1 db-ot szeretnénk megrendelni!

1. Fluor Protection Shield for DM IL LED

2. Universal holding frame M

Universal holding frame M, suitable for fixed stages with object guide of inverted microscopes DM IL, DM IRB or DM IRE2. Using the Universal Mounting Frames M it is possible to fix petri dishes with diameters from 24 mm up to 68 mm or to fix slides with a length up to 120mm. Depending on the diameter and the height of petri dishes two movable holding devices are adjusted. Outer holder dimensions (LxWxH) in mm: 165 x 100 x 5

3. Slider for Lightrings S40, complete

Slider for Phase Contrast with 4 positions, 1x Brightfield and 3x light rings for condenser S40/0.45

4. Lamp housing 106Z left, Hg100W,1",6-lens

Lamp housing 106z, Hg 100W,(left-operation for inverted microscopes)metal lamphousing with side lamp access, with centerable lamp mount for Hg 100W lamp, with 1.5 m power cable. 6 lenses, achromatic 1-inch collector, UV optimized transmission > 50% at 340nm, centerable reflector for doubling the focal point and optimization of the illuminated area, with heat absorbing filter, without burner.

5. Power supply EBQ 100-04-L

Suplly unit Hg 100W. Automtic switching to power supply voltage 90V - 250V, 50/60Hz with operating hours display, including power cord

6. Hg gas discharge lamp 103 W/2

HIGH PRESSURE BURNER 103 W / 2

7. Height adjusting plate for DM IL, 20mm

Height adjusting plate for DMIL. Arises the DMIL by 20 mm for ergonomic reasons or to adapt the 100W Hg lamp house.

8. Filter system N2.1 S

Filter system N2.1 (small)for green excitation, excitation filter: BP 515- 560, dichromatic mirror: 580, suppression filter: LP 590

9. Filter system L5 ET, s